Transformer Winding Specification 2

Core: PQ26/20
Bobbin: Vertical/Terminal Pins 6-6(12pins) or compatible
AL – Value: 182.61 nH/N²
Inductance (1 – 3 pin): 250 µH (0.250 mH ±10%)
Copper wire current density: 6 A/mm²
Primary to secondary isolation: ≥ 4kV

Coil	Pin number	Number of turns	Wire gauge
Np1	‘3-2	18	SWG #26
Ns1	‘11-9	23	SWG #25
Ns3	‘9-8	5	SWG #25
Nd	‘5-6	8	SWG #29
Ns4	‘10-7	5	SWG #25
Ns2	‘12-10	23	SWG #25
Np2	‘1-2	19	SWG #26

Winding direction: Uniformed