Transformer Winding Specification 1

Core: PQ26/20
Bobbin: Vertical/Terminal Pins 6-6(12pins) or compatible
AL – Value: 182.61 nH/N²
Inductance (1 – 3 pin): 260 µH (0.26 mH ±10%)
Primary to secondary isolation: ≥ 4kV

Coil	Pin number	Number of turns	Wire gauge
Np1	‘3-2	18	SWG #21
Ns1	‘11-9	28	SWG #20
Nd	‘5-6	10	SWG #23
Ns2	‘12-8	28	SWG #20
Np2	‘1-2	19	SWG #21

Winding direction: Uniformed